## Slide 1: working principle of midi interface
Md. Fazle Rabbi
ID:16CSE057

## Slide 2: Musical Instrument Digital Interface

## Slide 3: MIDI Basics
First introduced in 1983
MIDI isn’t hardware or software
It’s a universal “digital language” and means of communication for music technology

## Slide 4: MIDI Basics
MIDI consists of performance information—like print music

## Slide 5: MIDI Basics
MIDI is completely independent of the audio circuitry—it’s not sound.
L R AUDIO
IN OUT THRU
MIDI
Note On; Note Number; Velocity; Note Off

## Slide 6: MIDI
MIDI doesn’t transmit digital audio.
What it does transmit is the basic information supplied by the performer:
  What keys are pressed/released, and when
  What pedals are pressed etc.

## Slide 7
MIDI devices communicate using messages…
m e s s a g e s
Note on
Note off
Program change
Pitch bend
Controller change
Pressure (polyphonic)
Pressure (monophonic)
Notes: 7

## Slide 8: MIDI Specification – The Techie Bit
Physically MIDI is:
  A simplex asynchronous serial interface
    Simplex – data only flows in one direction, from transmitter to receiver
    Serial – bits of data are transmitted one at a time in series (rather than all at once in parallel)
    Asynchronous – the duration of each bit is fixed (32 µs for MIDI). Both the transmitter and receiver need a separate accurate clock to measure this duration. No clock signal is transmitted so only a single pair of wires is needed.
  Baud rate = 31250 bits/second
  Data is transmitted in 8-bit packets with one start bit, one stop bit and no parity.

## Slide 9: Digital Serial Communications
time
LSB
MSB
Start bit (always 0)
Stop bit (always 1)
Data bits
320 s
1
0
Eg. To transmit (105)10 = (01101001)2
Start
bit
Stop
bit
1
0
0
1
0
1
1
0
Start bit detected
48 µs
1
0
32 µs
0
32 µs
1
0
1
1
0
32 µs
32 µs
32 µs
32 µs
32 µs

## Slide 10: MIDI Connections
Most MIDI devices have three sockets:
  MIDI In: Receives MIDI information
  MIDI Out: Transmits MIDI information
  MIDI Thru: Repeats exactly the ‘MIDI In’ signal
Using the ‘Thru’ socket, more than one instrument can be controlled by a single MIDI output:
IN
OUT
THRU
IN
OUT
THRU
IN
OUT
THRU
A
B
C

## Slide 11: MIDI Connections
MIDI Ports
IN OUT THRU
IN – Receives MIDI information
OUT – Transmits MIDI information
THRU – Passes along MIDI information
To next
MIDI IN

## Slide 12: MIDI Connections
MIDI Cable
A cable with a 5-pin DIN connector on each end.

## Slide 13: MIDI Connections
MIDI “Master” instrument
The instrument that sends information
Master
IN OUT THRU
Slave
IN OUT THRU
MIDI “Slave” instrument
The instrument that receives information

## Slide 14: Computers & MIDI
Connecting a MIDI Interface
IN OUT

## Slide 15: Computers & MIDI
MIDI Interface
A device that is used to connect a computer to a MIDI system
Provides the MIDI IN and OUT ports for connection to a MIDI device
Translates MIDI data into a computer’s own machine language

## Slide 16
Multi-port MIDI Interface (2 in/out pairs)
IN
A B
OUT
A B
USB port
Thru switch – connects In to Out,
for use without a computer
Leave in ‘out’ position!
Lights!
Notes: 16

## Slide 17
Multi-port MIDI Interface (8 in/out pairs)
Front
Back
MIDI Outputs
MIDI Inputs
USB port
Each MIDI cable can carry 16 channels.
Notes: 17

## Slide 18: MIDI Messages
All that the physical MIDI interface does is allow the transmission and reception of 8-bit numbers
To play music, a language or protocol is needed to make sense of the numbers
MIDI uses messages consisting of one or more bytes
Most messages use 2 or 3 bytes in this format:
Status Byte
Data Byte 1
Data Byte 2
1
0
0
Message Type
Channel No.
Data 1 (0-127)
Data 2 (0-127)

## Slide 19: Status Bytes and MIDI Channels
All MIDI messages begin with a status byte
  The most significant bit of a status byte is always ‘1’, for any other byte, it is ‘0’
  Bits 4,5 and 6 of the status byte indicate the message type (giving eight possible messages)
  The lowest 4 bits hold the channel number
  MIDI devices can be set to only respond to a particular channel number, allowing up to 16 instruments to be independently controlled from a single MIDI output
Status Byte
Data Byte 1
Data Byte 2
1
0
0
Message Type
Channel No.
Data 1 (0-127)
Data 2 (0-127)

## Slide 20: Message Types
Data
Data
System Message
111
MSByte
LSByte
Pitch Bend
110
(not used)
Pressure
Channel Aftertouch
101
(not used)
Program Number
Program Change
100
Value
Controller Number
Control Change
011
Pressure
Note Number
Polyphonic Aftertouch
010
Velocity
Note Number
Note On
001
Velocity
Note Number
Note Off
000
Data Byte 2
Data Byte 1
Message Type
Message bits

## Slide 21: Note On/Off
When a key is pressed, a note-on message is transmitted
When a key is released, a note-off message is transmitted
C3
60
D3
62
E3
64
F3
65
G3
67
A4
69
B4
71
A#4
70
G#3
68
F#3
66
D#3
63
C#3
61
C2
48
D2
50
E2
52
F2
53
G2
55
A3
57
B3
59
A#3
58
G#2
56
F#2
54
D#2
51
C#2
49
Status Byte
Data Byte 1
Data Byte 2
1
0
0
Off/On
Channel No.
Note Number (0-127)
Velocity (0-127)
0
0
0/1

## Slide 22: Example
No key pressed
Action
MIDI message
MIDI Output
Nothing
Idle
F3 released
Note Off, F3, Velocity=55
10000000, 01000001, 00110111
(128, 65, 55)
F3 pressed
Note On, F3, Velocity=100
10010000, 01000001, 01100100
(144, 65, 100)
F3 Held
Nothing
Idle

## Slide 23: Control Change
Other than the keyboard, several other controls affect the sound e.g. the volume knob, sustain pedal, modulation wheel etc.
When any of these controls are adjusted, the new value is transmitted using a control change message.
Controller number identifies the control to be altered (e.g. 1 = modulation, 7 = volume)
The value can be either:
  A number between 0 and 127 for continuous controllers
  Either 0 or 127 indicating ‘off’ and ‘on’ for switches
Status Byte
Data Byte 1
Data Byte 2
1
0
0
Channel No.
Controller Number (0-127)
Value (0-127)
0
1
1

## Slide 24
THE END